# Text boxes

# Dimensions

Overall Cabinet:  45 5/8"H x 25 3/4”W x 22”D

Inside:  		  38 1/2”H x 23 ½”W x 17 ¼" D

Weight:  	   515 lbs.

Accessories:        2 adjustable shelves

1 locking drawer

(drawer is 3”H x 22”W x 16 ¾”D)

Safe Construction

Insulation is fully encased between an inner and outer wall, keeping it out of contact with the records, and out of the bolt work and locking mechanisms.  Safe body is made using .20 gauge steel in a uni-body construction to provide an elegant look while providing optimal structural strength.

# Door Handle

Attractive and sturdy, handle is easy to grip and turn.

# Safe Doors

Safe outer door is made of welded steel and are insulated with our proprietary insulation.  Each outer door interlocks with the safe body to make safe interior resistant to heat transfer using a labyrinth sealing system.  Special gaskets prevent water damage caused by fire hose spray or sprinklers.

Bolt Down Kit

Safe is pre-drilled and includes all the hardware needed to bolt the safe to the floor for additional security.

# Fire Resistance & Impact Rating

These safes carry the prestigious SP classification NT Fire 017 120 Paper which includes a two-hour fire test at 1850°F.  It has also been tested and certified for impact resistance during a 30’ fall and a 2000°F explosion test in compliance with KIS standards.  The safe’s certification is considered equal to the UL Class 350 - 2 Hr. Fire & Impact resistance classification.

Safe Purpose

Fire Commander safes are used to protect information stored on paper and also limited types of computer media such as CDs, DVDs, flash drives, and memory cards.  Safes are usually placed in offices, records rooms, or at an off-site location for archival storage.

Insulation

Phoenix’s proprietary insulation is asbestos-free, and uses modern age chemistry principles to provide outstanding fire protection.  Insulation also provides protection for the safe contents against magnetic interference.

# Security Lock

Fire Commander safes use user-friendly digital lock to secure the safe.

# Finish

Phoenix Fire Commander safes are painted with an extremely durable water-based, air-dry, textured enamel paint finish.

# Color

Phoenix Commander safes are available in a neutral RAL9002 off-white color.

# Product Warranty

All Phoenix products carry a three-year parts and labor warranty.

# Free After A Fire Replacement

If your Phoenix Commander safe is exposed to a fire, Phoenix will replace the safe free!

1/25/13

All weights & sizes are approximate.  Phoenix policy is one of constant improvement.  We therefore reserve the right to alter any part of the specification achieved in this publication without notice

### Phoenix Safe International LLC

### PO Box 608

Lebanon, IN  46052-0608

800-636-0778

Fax 765-483-0962

www.phoenixsafeusa.com

Model     1901

Phoenix Fire Commander Safe Specifications