# Text boxes

# Security Lock

DataCommander safes use a sophisticated digital lock to secure the safe.  The interior doors do not lock, but use a special latching mechanism to provide pressure to create a secure closure.

# Finish

Phoenix DataCommander safes are painted with an extremely durable water-based, air-dry, textured enamel paint finish.

# Color

Phoenix DataCommander safes are available in a neutral RAL9002 off-white color.

# Product Warranty

All Phoenix products carry a three-year parts and labor warranty.

# Free After a Fire Replacement

If your Phoenix DataCommander safe is exposed to a fire, Phoenix will replace the safe free!

Max Capacities of Popular Media*

LTOs -	 858 or    DLT – 	924 or

8MM – 1938 or	4MM – 3944 or

CDs/DVDs – 2664

*with easy accessibility

Additional multimedia drawers may be needed to achieve max capacities.

# Dimensions

Overall Cabinet:  68 ¾"H x 27 ½”W x 28 ½”D

Inside Compartment:    55 3/4”H x 15 ½”W x 15 ¾ " D

Weight:  1250 lbs.

Standard Accessories: (5) MD4620D0508 multimedia drawers & (2) S4620 adjustable shelves

# Fire Resistance & Impact Rating

These safes carry the prestigious SP classification NT Fire 017 120 Diskette which includes a two-hour fire test at 1850°F and a 2000°F explosion test.  It has also been tested and certified for impact resistance during a 30’ fall in compliance with KIS standards.  The safe’s certification is considered equal to the UL Class 125 - 2 Hr. Fire & Impact resistance classification.

Safe Purpose

DataCommander data safes are used to protect information stored on all types of computer media, including tape cartridges, CDs, DVDs, removable hard drives, flash drives, memory cards, microfilm, etc.  Safes are usually placed very close to the main server or computer in the computer room, or at an off-site location for archival storage.

Insulation

Phoenix’s proprietary insulation is asbestos-free, and uses modern age chemistry principles to provide outstanding fire protection.  Insulation also provides protection for the safe contents against magnetic interference.

9/28/11

All weights & sizes are approximate.  Phoenix policy is one of constant improvement.  We therefore reserve the right to alter any part of the specification achieved in this publication without notice

### Phoenix Safe International LLC

### PO Box 608

Lebanon, IN  46052-0608

800-636-0778

Fax 765-483-0962

www.phoenixsafeusa.com

Safe Construction

Insulation is fully encased between an inner and outer wall, keeping it out of contact with data and out of the bolt work and locking mechanisms.  Safe body is made using .20 gauge steel in a uni-body construction to provide an elegant look while providing optimal structural strength.

# Door Handles

Attractive and sturdy, handles are easy to grip and turn.

# Safe Doors

Safe outer doors are made of welded steel and are insulated with our proprietary insulation.  Each outer door interlocks with the safe body to make safe interior resistant to heat transfer using a labyrinth sealing system.  Special gaskets prevent water damage caused by fire hose spray or sprinklers.

Data safes also have an internal door treated with an insulating material that works with the insulating material of the outer safe to provide an internal compartment that will not exceed 125°F or 80% humidity during a fire.

Model     4622

Phoenix DataCommander Data Safe Specifications