# Text boxes

Phoenix World Class Vertical File Specifications

# Fire Resistance & Impact Rating

The file carries the prestigious SP classification NT Fire 017 60 Paper which includes a one-hour fire test at 1700°F and a 2000°F explosion test.  It has also been tested and certified for impact resistance during a 30’ fall in compliance with KIS standards.  The file’s certification is considered equal to the UL Class 350 -1 Hr. Fire & Impact resistance classification.

MTC Grade B Rating

This file now carries the prestigious MTC Grade B – 30 minute rating, certifying that certain types of less sensitive computer media (such as CDs, DVDs, USBs, flash drives, and memory sticks) can be safely stored inside.

Insulation

Phoenix’s proprietary insulation is asbestos-free, and uses modern age chemistry principles to provide outstanding fire protection.  Insulation between each drawer makes each drawer a separate insulated container.

Inner Steel Jacket

Insulation is fully encased between an inner and outer steel wall, keeping it out of contact with documents and out of the file suspension and locking mechanism.

# File Body

File body is made using .20 gauge steel using a uni-body construction style to provide an elegant look while maintaining structural strength.

# Drawer Pulls

Attractive, sturdy, recessed metal drawer pulls contain easy-to-read label holders.

# Drawer Suspensions

Phoenix uses a sturdy cradle suspension that is securely mounted to the file body.

Drawer Bodies

Each drawer body has high sides for use with legal hanging folders.  Movable dividers for manila folder filing are also included in each drawer.

# Drawer Heads

Drawer heads are made of welded steel and are insulated with our proprietary insulation.  Each drawer head interlocks with the file body to make drawers resistant to heat transfer using a labyrinth sealing system.  Special gaskets prevent water damage caused by fire hose spray or sprinklers.

# Locks

Phoenix files use a standard plunger lock that when engaged locks all drawers.

# Lock Bypass

Each file drawer is equipped with a lock bypass mechanism that enables the file user to allow a drawer to remain unlocked and accessible even when the file is locked.

# Finish

Phoenix World Class files are painted with an extremely durable water-based, air-dry, textured enamel paint finish.

# Colors

Phoenix World Class insulated files are available in black and putty colors.

# Product Warranty

All Phoenix files carry a three year parts and labor warranty.

# Free After A Fire Replacement

If your Phoenix fire file is exposed to a fire, Phoenix will replace the file free!

### Phoenix Safe International LLC

### PO Box 608

Lebanon, IN  46052-0608

800-636-0778

Fax 765-483-0962

www.phoenixsafeusa.com

# Dimensions

Overall Cabinet:  54” H x 19 ⅞" W x 25" D

Inside Drawer:    10¾” H x 15" W x 20" D

Weight:  471 lbs.

All weights & sizes are approximate.  Phoenix policy is one of constant improvement.  We therefore reserve the right to alter any part of the specification achieved in this publication without notice.

Model     LGL4W25

1/12/12